## Slide 1: ObjectFlow for Microcontrollers
Simple and Reliable Data Flow Graph programming for embedded applications

## Slide 2: ObjectFlow
Data-driven programming for tiny microcontrollers
Arduino Uno class (2KB/32KB) and larger
Small library, no central executive, timer- and communication event-driven
Similar to IEC61499, Node-RED, etc. based on Data Flow Graphs (DFG)
Uses the LWM2M data model and semantics with an event-driven communication protocol
Communication is implemented at the application layer using a set of well-known LWM2M types

## Slide 3: ObjectFlow - Digital Twin for Embedded Code
On-device code is simple, minimal, and reliable
A small set of primitives implemented as static C++ wrapper classes for Object and Resource
Graphs are build from a standardized JSON format that models Object and Resource Instances on the embedded device – a digital twin of the device code
Tools construct a C++ header file template that is built with the device code application handler bundle using the standard IDE (e.g. Arduino IDE), and downloaded to the device in the usual way.

## Slide 4: ObjectFlow – DFG wrapper
A small set of Resource types for communication
  Time types for Current, Interval, and LastActivation
  Input and Output link types based on LWM2M Objlink
  Subtypes for Input, Output, and Current Value
DFG - communication is event driven and initiated according to application logic
  Bound methods implement application handlers
  InputSync (data pull) and OutputSync (data push)
  onValueUpdate, onValueSync, onInterval handlers

## Slide 5: ObjectFlow – DFG architecture
An ObjectFlow application is a Data Flow Graph
DFG Nodes are implemented as LWM2M Objects
A DFG Node is a collection of one or more Objects
LWM2M Object Links (Objlink) are used to group Objects into a DFG Node and to implement the data flow connections between Nodes (arcs, edges)

## Slide 6: ObjectFlow - Tools
The DFG model tools do all of the heavy lifting so the embedded code can be extremely simple and lightweight, e.g. static typing is done in the model
Code generation involves serialization of the objects and resources into a c++ header file, and packaging of the implementation code for the application objects (time and data event handlers)
The result is a standard C++ package that can be built by any C++ toolchain (Arduino, etc.)