## Slide 1: ObjectFlow for Microcontrollers
Simple and Reliable Data Flow Graph programming for embedded applications

## Slide 2: ObjectFlow
Data-driven programming for tiny microcontrollers
Arduino Uno class (2KB/32KB) and larger
Small library, no central executive, timer- and communication event-driven
Similar to IEC61499, Node-RED, etc. based on Data Flow Graphs (DFG)
Uses the LWM2M data model and semantics with an event-driven communication protocol
Communication is implemented in the application layer using a set of standardized LWM2M types

## Slide 3: ObjectFlow - Digital Twin for Embedded Code
On-device code is simple, minimal, and reliable
A small set of primitives implemented as static C++ wrappers for application Objects and Resources
Graphs are build from a standardized JSON format that models Object and Resource Instances on the embedded device – a digital twin of the device code
Tools construct a C++ header file template that is built with the device code application handler bundle using the standard IDE (e.g. Arduino IDE), and downloaded to the device in the usual way.

## Slide 4: High Level Process
C++ Code
Build
Models
Models
JSON Models

## Slide 5: ObjectFlow – DFG wrapper
A small set of Resource types for communication
  Time types for Current, Interval, and LastActivation
  Input and Output link types based on LWM2M Objlink
  Value subtypes for Input, Output, and Current Value
DFG - communication is event driven and initiated according to application logic
  Bound methods implement application handlers
  InputSync (data pull) and OutputSync (data push)
  onValueUpdate, onValueSync, onInterval handlers

## Slide 6: ObjectFlow – DFG and Reactive Communication
CurrentValue
InputValue
OutputValue
InputLink
OutputLink
LWM2M Object
CurrentValue
InputValue
OutputValue
InputLink
OutputLink
LWM2M Object
onValueUpdate
outputSync
handler
handler
handler
handler
handler
handler
handler
handler

## Slide 7: Complex Functions
Value
In Link 1
In Link 2
In Value 1
In Value 2
Value
Value
Out Link
Out Value
Timer
Input Objects
Output Objects
Function Object
(Trigger)

## Slide 8: ObjectFlow – DFG architecture
An ObjectFlow application is a Data Flow Graph
DFG Nodes are implemented as LWM2M Objects
A DFG Node is a collection of one or more Objects
LWM2M Object Links (Objlink) are used to group Objects into a DFG Node and to implement the data flow connections between Nodes (arcs, edges)

## Slide 9: Example graph
TimeSource: Type: TimeSource IntervalTime: 1000 TimerOutputLink: AnalogInput AnalogInput: Type: AnalogInput GpioPinID: 7 IntervalTime: 0 OutputLink: MapToCelsius MapToCelsius: Type: ValueMap InputLowScale: 0 InputHighScale: 1023 CurrentLowScale: 0 CurrentHighScale: 100 CurrentValueMinimum: 0 CurrentValueMaximum: 100 CurrentValueUnit: C OutputLink: Display Display: Type: Publisher InputValue: { ValueType: IntegerType }

## Slide 10: ObjectFlow - Tools
The DFG model tools do all of the heavy lifting so the embedded code can be extremely simple and lightweight, e.g. typing is done in the model
Code generation involves serialization of the objects and resources into a C++ header file, and packaging of the implementation code for the application objects (time and data event handlers)
The result is a standard C++ package that can be built by any C++ toolchain (Arduino, etc.)

## Slide 11: High Level Process
SDF Models
Flow JSON
C++ Header
UML Doc
C++ Classes
Model Build
Target Build
SDF Models

## Slide 12: Build Process
SDF
SDF
SDF
SDF
DSL
Flow JSON
Flow JSON
Flow JSON
Models
Build SDF Instances
Fully Resolved Instances
C++ Header
Embedded Code
SDF
Select + Copy
Configure
Merge
Merge
Serialize
Code Gen
Flow UML
Render
YAML UML
TD
Render
Documents
YAML
UML
WoT TD

## Slide 13: Making a New Flow Graph
Flow JSON
Build
UML Doc
Target
UML Doc

## Slide 14: Making a New Object Type
New SDF Model
New C++ Class
C++ Classes
C++ Classes
C++ Classes
C++ Classes
SDF Models
SDF Models
SDF Models
SDF Models
Build
types.h
Co-develop

## Slide 15: Example SDF Model
defaultnamespace: objectflow sdfData: # add this ObjectType ID to the TypeID registry TypeID: ObjectType: Publisher: { const: 43008 } sdfThing: # Publisher Object Publisher: sdfRef: /#/sdfThing/ObjectFlowObject sdfData: TypeID: sdfRef: /#/sdfData/TypeID/ObjectType/Publisher # Publisher Object Resources sdfRequired: - /#/sdfThing/Publisher/sdfThing/InputValue sdfThing: InputValue: sdfRef: /#/sdfThing/ObjectFlowObject/sdfThing/InputValue ValueType: sdfChoice: default: { sdfRef: /#/sdfData/ValueType/sdfChoice/IntegerType } sdfAction: OnDefaultValueUpdate: Publish the data to the endpoint
=> TypeID: { const: 43008 }

## Slide 16: Example SDF Instance
defaultnamespace: objectflow sdfThing: # Instance Graph InstanceGraph: sdfRef: /#/sdfThing/ObjectList # Objects in the graph sdfThing: TimeSource: sdfRef: /#/sdfThing/TimeSource sdfThing: IntervalTime: sdfProperty: Value: sdfChoice: IntegerType: { const: 1000 } OutputLink: sdfData: SdfLink: { InstancePointer: /#/sdfThing/InstanceGraph/sdfThing/AnalogInput } AnalogInput: sdfRef: /#/sdfThing/AnalogInput sdfThing: GpioPinID: sdfProperty: Value: sdfChoice: IntegerType: { const: 7 } OutputLink: sdfData: SdfLink: { InstancePointer: /#/sdfThing/InstanceGraph/sdfThing/ScaleMapper }

## Slide 17: Simplified DSL
defaultnamespace: objectflow sdfThing: # Instance Graph InstanceGraph: sdfRef: /#/sdfThing/ObjectList # Objects in the graph sdfThing: TimeSource: sdfRef: /#/sdfThing/TimeSource sdfThing: IntervalTime: sdfProperty: Value: sdfChoice: IntegerType: { const: 1000 } TimerOutputLink: sdfData: SdfLink: { InstancePointer: /#/sdfThing/InstanceGraph/sdfThing/AnalogInput } AnalogInput: sdfRef: /#/sdfThing/AnalogInput sdfThing: GpioPinID: sdfProperty: Value: sdfChoice: IntegerType: { const: 7 } OutputLink: sdfData: SdfLink: { InstancePointer: /#/sdfThing/InstanceGraph/sdfThing/MapToCelsius }
TimeSource: Type: TimeSource IntervalTime: 1000 TimerOutputLink: AnalogInput AnalogInput: Type: AnalogInput GpioPinID: 7 OutputLink: MapToCelsius

## Slide 18: Reserved LWM2M Types
TypeID: ResourceType: ValueType: { const: 27000 }
InputLinkType: { const: 27001 } OutputLinkType: { const: 27002 } InputValueType: { const: 27003 } CurrentValueType: { const: 27004 } OutputValueType: { const: 27005 } CurrentTimeType: { const: 27006 } IntervalTimeType: { const: 27007 } LastActivationTimeType: { const: 27008 }
#define InputLinkType 27000
#define InputLinkType 27001 #define OutputLinkType 27002 #define InputValueType 27003 #define CurrentValueType 27004 #define OutputValueType 27005 #define CurrentTimeType 27006 #define IntervalTimeType 27007 #define LastActivationTimeType 27008
SDF Definition
Generated C++ Header

## Slide 19: Resolved Instance Graph